## Slide 1
Sensitivity Analysis and Surrogate Modeling of PEM Fuel Cells
Presented by:
Dejvis Toptani
Nathaly Vergel Serrano
Camila Bermudez Valderrama
August 1st, 2025
Supervised by: Dr. Giuseppe Casalicchio
In collaboration with:
Luis Winkler (ZSW Ulm)
Prof. Herbert Palm (UAS Munich)

## Slide 2
Outline
1. Motivation: Understanding PEMFC
2. Model validity
3. Sensitivity analysis
4. Surrogate modeling
5. Future work

## Slide 3
Motivation
Understanding Proton Exchange Membrane (PEM) Fuel Cells
Notes: PEM fuel cells are central to the transition toward clean energy. However, modeling them accurately involves solving complex systems of differential and algebraic equations, which can be computationally expensive. This limits their practical utility in fast design or optimization pipelines. That’s why our project focused on identifying the most influential parameters through sensitivity analysis, and using that insight to build an analytical and interpretable surrogate model, that is, a simplified faster version that retains key behavior.

## Slide 4: Understanding PEMFCs through surrogates
Model Validity | Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
Figure 1. Operating principle of a PEM fuel cell: hydrogen and oxygen react to produce electricity and water. Source: Wikipedia - PEM fuel cell
Challenges with models
PEMFCs’ complex behaviour is only partially understood
Modeled using accurate but expensive physics-based simulators (e.g. AlphaPEM)
Models have no closed form: they rely on solving complex DAEs
Goal of project partners
Perform model calibration using Fisher Information Matrix-based Optimal Experimental Design (FIM-OED)
They need an analytically closed-form surrogate model that
  allows faster simulations
  enables exact partial derivative computation
What are PEM Fuel Cells?
Proton Exchange Membrane (PEM) fuel cells (FC) convert hydrogen and oxygen into electricity, emitting only water as subproduct.
Used in automotive and backup power systems
Promising for a clean energy future!
Notes: Context:
PEM Fuel Cells are modeled via high-fidelity physics-based simulations (e.g., AlphaPEM).
These models are accurate but rely on solving complex DAEs and require significant computational time.
Model outputs depend on many undetermined physical parameters (e.g., porosity, kinetics) that must be calibrated to match real system behavior.
Challenge:
To calibrate these parameters systematically, the team wants to use Optimal Experimental Design (OED) based on the Fisher Information Matrix (FIM).
FIM-based methods require efficient access to model derivatives (∂output/∂parameter).
Problem:
Current models are black-box or numerical → No analytical form → Derivatives must be approximated → Expensive, noisy, or unstable.
Goal:
Develop an analytical closed-form surrogate model of the PEMFC behavior.
Use techniques like symbolic regression (e.g., PySR) to derive interpretable, differentiable expressions that:
  - Accurately mimic the simulation outputs.
  - Enable fast and exact computation of derivatives.
  - Serve as a foundation for FIM-based OED and robust parameter calibration.

## Slide 5: Project goals: From Sensitivities to Surrogates
Model Validity | Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
We work with AlphaPEM, a 1D physics-based PEM fuel cell model using differential-algebraic equations (DAEs) to simulate polarization behaviour (current-voltage relation).
Gass et al, (2025)
Sensitivity Analysis (SA)
Identify and quantify the influence of input features on AlphaPEM
Select a subset of most influential features
01
Surrogate Model (SM)
Develop an analytically closed-form surrogate model
Uses key features from SA
Faithful to AlphaPEM
Interpretable and computationally efficient
02
Notes: Problem
Proton Exchange Membrane (PEM) fuel cells are promising clean energy sources, especially for high-power applications like electric vehicles and backup systems. However, understanding how they operate—especially when integrated into complex systems like powertrains—is still challenging. Existing physical models are often too complex and computationally demanding, making them impractical for real-time analysis or optimization.

## Slide 6: Input-Output framework for AlphaPEM
Model Validity | Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
Input features
Variable (19)
Operating conditions (7)
Undetermined physical parameters (12)
Fixed (14)
Accesible physical parameters (7)
Current density parameters (7)
AlphaPEM
Black-box, complex simulator
Functional output
Evaluates performance under different loads and operating conditions
Polarization curve (PC)
Sensitivity analysis
Figure 2: AlphaPEM is a “black-box” simulator that maps a given configuration (a combination of physical parameters and operating conditions) to a polarization curve, characterizing fuel cell performance.

## Slide 7
IRD| Sensitivity Analysis | Surrogate Model | Conclusions and next steps
1. Introduction and motivation
Goals
  Conduct a sensitivity analysis (SA) on the AlphaPEM model to identify and quantify the influence of the input features on the performance of PEM fuel cells.
  Using the features from the SA develop an interpretable and analytically closed-form surrogate model that captures key behaviors of the AlphaPEM model while maintaining accuracy, with a focus on interpretability and computational efficiency.
1
2
- Sobol analysis
- TreeSHAP
Sensitivity Analysis
Interpretable Regional Descriptors
Model validy
Symbolic regression
Surrogate model
Notes: Check the text the scheme

## Slide 8
Problem
Model Validity| Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
  → Their behavior in real-world applications remains partially understood.
  → Existing models are accurate but computationally demanding.
  → Proton Exchange Membrane (PEM) fuel cells are complex clean-energy systems combining physical and electrochemical processes.
Notes: Problem
Proton Exchange Membrane (PEM) fuel cells are promising clean energy sources, especially for high-power applications like electric vehicles and backup systems. However, understanding how they operate—especially when integrated into complex systems like powertrains—is still challenging. Existing physical models are often too complex and computationally demanding, making them impractical for real-time analysis or optimization.

## Slide 9
Model Validity
Parameter ranges in which the model is valid
Notes: We started by sampling across the full input space defined by expert- and literature-based ranges. However, we quickly noticed that many configurations were invalid — meaning the model produced unphysical results or numerical errors. Since AlphaPEM takes 1.5 minutes per run, this was inefficient. This led us to focus on the concept of model validity: defining which parts of the input space actually yield usable simulation results.

## Slide 10: Asessing the Model Validity of AlphaPEM
Sensitivity Analysis | Surrogate Model | Future Work
2. Model validity
Motivation
Finding the region of the input hyperspace where AlphaPEM leads to a physically meaningful, simulation-successful polarization curve.
What’s model validity?
Sampling in high dimensions: Why model validity matters
We “sample” AlphaPEM by varying 19 input parameters independently
Project partners and author (Gass, 2025) provided wide ranges
However:
(!) Many configurations yield invalid outputs (e.g. negative or excessive voltages)
(!) AlphaPEM is expensive (≈1.5 min per run) → computationally wasteful
Notes: Motivation to use IRD – we were sampling from the whole space

## Slide 11: Goal: Finding a valid hyperbox
Sensitivity Analysis | Surrogate Model | Future Work
2. Model validity
Motivation
What’s a valid
polarization curve?
It starts within the expected voltage range (0.0–1.23 V)
Decreases monotonically (within a 5 mV tolerance) with current density
It maintains positive voltage at and mid current densities (until 2.0 A/cm²)
Find a region (hyperbox) where sampled configurations are consistently valid. That is, the probability of finding a valid polarization curve is very high (>0.9)
Figure 3: Valid polarization curve: within 0–1.23 V, monotonic, and positive up to 2.0 A/cm². Source: ResearchGate
Notes: Motivation to use IRD – we were sampling from the whole space

## Slide 12
Sensitivity Analysis | Surrogate Model | Future Work
2. Model validity
Motivation
04
Valid hyperbox
A box-constrained region where AlphaPEM simulations are likely valid
02
Training a classifier
Model: Random Forest
→ Predicts the prob. a config will yield a valid output
→ Metrics (test set): Precision = 0.91, F1-score = 0.94
01
Labeled configs
Input: 2000+ configs labeled as valid or invalid based on resulting PCs
Roughly balanced dataset
03
Find valid region
Method: PRIM
(peeling & pasting)
Goal: find largest hyperbox around a reference valid config with ≥90% validity rate
Valid
Invalid
Interpretable Regional Descriptors (IRD) Hyperbox-based local explanations
IRDs are interpretable hyperboxes in input space where a model’s prediction remains stable
Originally used for model explanation, here applied to find regions yielding valid simulation outputs
We used the PRIM method, adapted to return a hyperbox with high validity precision
Dandl et al. (2022)
Notes: Motivation to use IRD – we were sampling from the whole space

## Slide 13
Sensitivity Analysis | Surrogate Model | Conclusions and next steps
2. IRD
Introduction and motivation
PARAMETERS
Notes: Motivation to use IRD – we were sampling from the whole space

## Slide 14
Sensitivity Analysis | Surrogate Model | Conclusions and next steps
2. IRD
Introduction and motivation
Sampling from AlphaPEM
  → Due to the lack of empirical data, we used Latin Hypercube Sampling to uniformly explore the full input space.
  → No dependencies between features were assumed.
What is a valid polarization curve?
→ It starts within the expected voltage range (0.0–1.23 V)
→ Decreases monotonically (within a 5 mV tolerance)
→ It maintains positive voltage at low current densities.
Notes: Motivation to use IRD – we were sampling from the whole space

## Slide 15
Sensitivity Analysis | Surrogate Model | Conclusions and next steps
2. IRD
Introduction and motivation
What is the Interpretable Regional Descriptors (IRD)?
IRD helps explain "where" in the input space certain types of output behavior occur.
How does it work?
Clustering and labeling output curves based on shape (validity criteria).
Training interpretable models (typically decision trees or rule-based classifiers) to map input features to curve types.
Generating regional descriptors: rules or conditions that explain which input combinations lead to each type of curve.
In R it is implemented in the package XXXXXX
What is the output?
Interpretable rules or regions
(e.g., "Region A: high humidity, low temperature → flat voltage curves").
Notes: What is IRD? How does it work? Where is it implemented?

## Slide 16
Sensitivity Analysis | Surrogate Model | Conclusions and next steps
2. IRD
Introduction and motivation
Our results!
Notes: Comparison of the results

## Slide 17
3. Sensitivity analysis
Camila

## Slide 18
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
What is a sensitivity analysis?
It is a method used to determine how changes in input variables influence the output of a model.
It helps identify which inputs have the most significant effect on the results and how robust the model is to variations or uncertainty in those inputs.
What is the Goal?
Quantify the influence of each input on the output.
Prioritize the most impactful variables.
Guide model simplification, optimization.
Increase understanding of the system's behavior under different conditions.

## Slide 19
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
Sobol Indices
Sobol analysis assumes the model can be decomposed additively
First-order (S1) : Individual effect
Since the model is decomposed this way, the total variance of the output can be split into components.
Sobol indices quantify how much of the output variance is due to each input (individually and via interactions).
Total-order (ST): Total effect including interactions
Second-order (S2):
pairwise interactions

## Slide 20
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
Set a baseline prediction:
the model's average output.
For a specific input:
1. Traverse the tree using the input's feature values.
2. Track which features are used along the decision path.
3. Reach a leaf and get the final prediction.
1
2
3
Compute the difference between the leaf prediction and the baseline. This is what needs to be explained.
Distribute the difference fairly among features using SHAP values, which reflect each feature’s influence by considering all possible combinations.
4
For ensembles (like random forests or gradient boosting):
Repeat las steps for each tree.
Sum SHAP values across all trees for each feature.
5
How TreeSHAP Works?
SHAP Values
SHAP (SHapley Additive exPlanations) values explain how much each feature contributes to a model’s prediction.
(for Trees and Forests)

## Slide 21
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
Pros & cons
Sobol Indices
SHAP Values
Global sensitivity quantifies how inputs influence output variance.
Accounts for interactions.
Applies to any model.
Offers a clear variance decomposition.
Local explanations clarify individual predictions.
Applies to any model.
Handle interactions.
They are grounded in fair game-theoretic principles, with guarantees of fairness and consistency.
High computational cost.
Assumes input independence.
Provides only global insights.
Struggles with high-dimensional data.
Computationally intensive.
May give misleading results if feature dependence isn't handled well.

## Slide 22
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
what we tried -> Sobol Alpha PEM- Sobol in XGBoost-SHAP in XGBoost

## Slide 23
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
SHAP Values
Sobol Indices
Pros
Cons
Global sensitivity: Measures how each input affects the entire output variance across the input space.
Handles interactions
Model-agnostic: Can be applied to any model or function.
Interpretability: Offers a clear decomposition of variance for explaining uncertainty.
Computationally expensive: Requires a large number of model evaluations.
Assumes inputs are statistically independent.
Less local: Only explain overall variable influence.
Becomes less practical for high-dimensional problems.
Local explanations: Explains individual predictions.
Model-agnostic or model-specific: Works with any model (TreeSHAP is efficient for tree-based models).
Handles feature interactions
Theoretically grounded: Based on game theory, with guarantees of fairness and consistency.
Computationally intensive.
May give misleading results if feature dependence isn't handled well.

## Slide 24
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
Regions
definition
Activation [0;0.4]
Ohmic [0.4; 1.6]
Mass transport [1.6; Inf]
Sampling strategy: Sobol sequences
It generates quasi-random sequences that are uniformly distributed sample points in high-dimensional spaces.
Calculating the Sobol indices over those configurations lead into more stable and consistent results, due to the uniformity of the samples.
They allow incrementally increase the sample size, while preserving and building upon previous points saving computing time.
Sample size:
  For calculating only first-order indices (S1): N × (D + 2)
  For both first-order (S1) and second-order (S2) indices: N × (2D + 2)

## Slide 25
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
Our results!

## Slide 26
4. Surrogate model
Dejvis

## Slide 27
Conclusions and next steps
4. Surrogate Model
Introduction and motivation | IRD | Sensitivity Analysis
PySR: Symbolic Regression in Python
Uses evolutionary algorithms to search for mathematical expressions to fit data
Discovers both the form and the parameters of the model
No assumption on functional form
Expressions are represented as trees
[Source] Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl

## Slide 28
Conclusions and next steps
4. Surrogate Model
Introduction and motivation | IRD | Sensitivity Analysis
Mutation
Crossover
[Source] Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl

## Slide 29
Conclusions and next steps
4. Surrogate Model
Introduction and motivation | IRD | Sensitivity Analysis
PySR Inner Loop
[Source] Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl

## Slide 30
Conclusions and next steps
4. Surrogate Model
Introduction and motivation | IRD | Sensitivity Analysis
PySR Outer Loop
[Source] Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl

## Slide 31
Conclusions and next steps
4. Surrogate Model
Introduction and motivation | IRD | Sensitivity Analysis
TÍTULO 1 | TÍTULO 2 | TÍTULO 3 | TÍTULO 4 | TÍTULO 5
Categoría 1 | What tool will we use for communication? (email/slack/other) | 20% |  | Approved
Categoría 2 | Are we going to hold recurrent meetings? What would be the frequency? | 40% |  | Approved
Categoría 3 | Who needs to know what, and how should we communicate that information? | 30/34% |  | 
Categoría 4 | How will you keep up-to-date on project status and anything blocking progress? | 50% |  | Approved
Categoría 5 | who makes what decisions and who approves what. | 23% |  | Approved

## Slide 32
Other administrative aspects | Technical questions
4. Communication plan
Team | Goals and outcomes | Timeframe
TÍTULO 1 | TÍTULO 2 | TÍTULO 3 | TÍTULO 4 | TÍTULO 5
Categoría 1 | What tool will we use for communication? (email/slack/other) | 20% |  | Approved
Categoría 2 | Are we going to hold recurrent meetings? What would be the frequency? | 40% |  | Approved
Categoría 3 | Who needs to know what, and how should we communicate that information? | 30/34% |  | 
Categoría 4 | How will you keep up-to-date on project status and anything blocking progress? | 50% |  | Approved
Categoría 5 | who makes what decisions and who approves what. | 23% |  | Approved

## Slide 33
5. Conclusions and next steps.

## Slide 34
Introduction and motivation | IRD | Sensitivity Analysis | Surrogate Model
5. Conclusions and next steps
Will be provided any kind of computational equipment/resources?
Is there any attention time to discuss questions in person?
Are there any kind of dependencies or constrains?

## Slide 35
Technical questions
Team | Goals and outcomes | Timeframe | Communication plan
5. Other administrative aspects
Will be provided any kind of computational equipment/resources?
Is there any attention time to discuss questions in person?
Are there any kind of dependencies or constrains?

## Slide 36
Team | Goals and outcomes | Timeframe | Communication plan | Other administrative aspects
6. Technical questions
What are your expectations for the surrogate model, should it be symbolic, physics-informed, or just accurate? Disponible en algunos idiomas. | What are the input features of AlphaPEM that we are going to include and what are their ranges? Para el Dr. Müller :V | Which variables of AlphaPEM are most uncertain or critical?
Do you already have preferred sensitivity analysis methods? | Is the model deterministic or does it include stochastic components? | Which are the target variables?
1.
2.
3.
4.
5.
6.
Preguntas de implementación

## Slide 37
Source Sans Pro Bold
Source Sans Pro

## Slide 38
Bibliography

## Slide 39
Bibliography
Falta el de alphaPEM
Dandl, S., Casalicchio, G., Bischl, B., & Bothmann, L. (2023). Interpretable Regional Descriptors: Hyperbox-Based Local Explanations (arXiv:2305.02780) [Preprint]. arXiv. https://doi.org/10.48550/arXiv.2305.02780

## Slide 40
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
JAN.
FEB.
MAR.
JUN.
JUl.
JUl.
AUG.
PREPROYECTO
Hacer algo
Hacer algo 2
PROYECTO
Hacer algo
Hacer algo 2
POSPROYECTO
Hacer algo
Hacer algo 2

## Slide 41
Timeframe | Communication plan | Other administrative aspects | Technical questions
2. Goals and outcomes
Team
What are the deliverables?
What is in the scope?
What is out the scope?
Scope

## Slide 42
Sensitivity Analysis | Surrogate Model | Conclusions and next steps
2. IRD
Introduction and motivation
What is the problem this project is trying to solve?
Why is it important for you?
What are the objectives?
Why now?
What are the key milestones?

## Slide 43
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com

## Slide 44
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com

## Slide 45
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com

## Slide 46
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com

## Slide 47
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com

## Slide 48
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com

## Slide 49
Thanks!
Dejvis Toptani - dtoptani@lmu.com
Nathaly Vergel Serrano - nvergels@lmu.com
Camila Bermudez Valderrama - cbermudezv@lmu.com