## Slide 1
Sensitivity Analysis and Surrogate Modeling of PEM Fuel Cells
Presented by:
Dejvis Toptani
Nathaly Vergel Serrano
Camila Bermudez Valderrama
August 1st, 2025
Supervised by:
Dr. Giuseppe Casalicchio
In collaboration with:
Luis Winkler (ZSW Ulm)
Prof. Herbert Palm (UAS Munich)
In collaboration with
University of Applied Sciences (UAS)
Munich
Center for Solar Energy and Hydrogen Research Baden-Württemberg

## Slide 2
Overview
01
Motivation
What are PEM fuel cells and why model them?
Surrogate Model
Can we build a faithful, but more efficient replica of the model?
04
Model Validity
Where does the model produce physically meaningful results?
02
Sensitivity Analysis
What are the most impactful input features?
03
Future Work
What are the next steps?
05

## Slide 3
1. Motivation
Understanding Proton Exchange Membrane (PEM) Fuel Cells

## Slide 4: Understanding PEMFCs through surrogates
Model Validity | Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
Figure 1. Operating principle of a PEM fuel cell: hydrogen and oxygen react to produce electricity and water.
Source: Wikipedia - PEM fuel cell
Challenges with simulators
PEMFCs’ complex behavior is only partially understood
Modeled using accurate but expensive physics-based simulators
Models have no closed form: they rely on solving complex DAEs
Goal of project partners
Perform model calibration using Fisher Information Matrix-based Optimal Experimental Design (FIM-OED)
They need an analytically closed-form surrogate model that
  allows faster simulations
  enables exact partial derivative computation
What are PEM Fuel Cells?
Proton Exchange Membrane (PEM) fuel cells (FC) combine hydrogen and oxygen to produce electricity, emitting only water as subproduct.
Used in automotive and backup power systems
Promising for a clean energy future!

## Slide 5
Project goals: From Sensitivities to Surrogates
Sensitivity Analysis (SA)
Identify and quantify the influence of input features on AlphaPEM
Select a subset of most influential features
01
Our simulator: AlphaPEM is an open source physics-based PEM fuel cell model that uses differential-algebraic equations (DAEs) to simulate polarization behavior.
Gass et al, (2025)
Model Validity | Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
Surrogate Model (SM)
Develop an analytically
closed-form surrogate model
Uses key features from SA
Faithful to AlphaPEM
Interpretable and computationally efficient
02

## Slide 6
Input features
Variable (19)
Operating conditions (7)
Undetermined physical parameters (12)
Fixed (14)
Accesible physical parameters (7)
Current density parameters (7)
AlphaPEM
Black-box, complex simulator
Functional output
Evaluates performance under different loads and operating conditions
Polarization curve (PC)
Sensitivity analysis
Figure 2: AlphaPEM is a “black-box” simulator that maps a given configuration (a combination of physical parameters and operating conditions) to a polarization curve, characterizing fuel cell performance.
Model Validity | Sensitivity Analysis | Surrogate Model | Future Work
1. Motivation
Input-Output framework for AlphaPEM
Source: Adapted from Gharbi et al. 2017. See Research Gate.

## Slide 7
2. Model Validity
Parameter ranges in which the model is valid

## Slide 8
Motivation
Finding the region of the input hyperspace where AlphaPEM leads to a physically meaningful, simulation-successful polarization curve.
What is model validity?
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
Asessing the Model Validity of AlphaPEM
Sampling in high dimensions: Why model validity matters
We “sample” AlphaPEM by varying 19 input parameters independently
Project partners and author (Gass, 2025) provided wide parameter ranges
However:
(!) Many configurations yield invalid outputs (e.g. negative or excessive voltages)
(!) AlphaPEM is expensive (≈1.5 min per run) → computationally wasteful
Figure 3: Illustration of model validity in a 2D input space. Each point is a tested configuration: red crosses are invalid, green dots are valid.

## Slide 9
Motivation
Finding the region of the input hyperspace where AlphaPEM leads to a physically meaningful, simulation-successful polarization curve.
What is model validity?
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
Asessing the Model Validity of AlphaPEM
Sampling in high dimensions: Why model validity matters
We “sample” AlphaPEM by varying 19 input parameters independently
Project partners and author (Gass, 2025) provided wide parameter ranges
However:
(!) Many configurations yield invalid outputs (e.g. negative or excessive voltages)
(!) AlphaPEM is expensive (≈1.5 min per run) → computationally wasteful
Figure 4: Illustration of model validity in a 2D input space. Each point is a tested configuration: red crosses are invalid, green dots are valid. “Safe zone” for sampling was added.

## Slide 10
What’s a valid polarization curve?
It starts within the expected voltage range (0.0–1.23 V)
Decreases monotonically (within a 5 mV tolerance) with current density
It maintains positive voltage at low and mid current densities (until 2.0 A/cm²)
Find a region (hyperbox) where sampled configurations are consistently valid. That is, where the probability of finding a valid polarization curve is very high (>0.9)
Figure 5: Valid polarization curve: within 0–1.23 V, monotonic, and positive up to 2.0 A/cm². Source: Replica of figure 3.2 from Gass’ thesis (Gass, 2024).
Motivation
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
Goal: Finding a valid hyperbox

## Slide 11
04
Valid hyperbox
A box-constrained region where AlphaPEM simulations are likely valid
→ Post-processed: Impurity = 0.00, distance = 0.087
02
Training a classifier
Model: Random Forest
→ Predicts the prob. a config will yield a valid output
→ Metrics (test set): Accuracy = 0.964, F1-score = 0.966
01
Labeled configs
Input: 2000+ configs labeled as valid or invalid based on resulting PCs
Roughly balanced dataset
03
Find valid region
Method: PRIM
(peeling & pasting)
Goal: find largest hyperbox around a reference valid config with ≥90% validity rate
IRDs are interpretable hyperboxes in input space where a model’s prediction remains stable
Here applied to find regions yielding valid simulation outputs
We used the PRIM method, adapted to return a hyperbox with high validity precision
Motivation
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
Interpretable Regional Descriptors (IRD)
Hyperbox-based local explanations
Dandl et al. (2022)

## Slide 12
 |  |  | Original range |  | Regional descriptor |  | 
 | Feature | Reference configuration | Lower | Upper | Lower | Upper | Range reduction (%)
Operational Condition | Tfc | 347.15 | 333.02 | 362.97 | 339.01 | 357.17 | 39%
 | Pa_des | 200000.00 | 130040.00 | 299920.00 | 138530.00 | 282930.00 | 15%
 | Pc_des | 200000.00 | 110040.00 | 297510.00 | 119410.00 | 269390.00 | 20%
 | Sa | 1.30 | 1.30 | 1.30 | 1.30 | 1.30 | 0%
 | Sc | 2.00 | 1.10 | 3.00 | 1.15 | 3.00 | 3%
 | Phi_a_des | 0.50 | 0.50 | 0.50 | 0.50 | 0.50 | 0%
 | Phi_c_des | 0.60 | 0.10 | 0.70 | 0.27 | 0.66 | 35%
Undetermined Physical Parameter | epsilon_gdl | 0.70 | 0.55 | 0.80 | 0.59 | 0.76 | 33%
 | tau | 1.02 | 1.00 | 4.00 | 1.00 | 3.57 | 14%
 | epsilon_mc | 0.40 | 0.15 | 0.40 | 0.16 | 0.40 | 4%
 | epsilon_c | 0.27 | 0.15 | 0.30 | 0.17 | 0.29 | 14%
 | e | 5 | 3 | 5 | 3 | 5 | 0%
 | Re | 5.70E-07 | 5.1E-07 | 5.0E-06 | 5.1E-07 | 4.8E-06 | 5%
 | i0_c_ref | 2.79 | 0.1 | 499.5 | 0.1 | 82.3 | 84%
 | kappa_co | 27.20 | 0.0 | 40.0 | 17.9 | 40.0 | 45%
 | kappa_c | 1.61 | 0.0 | 100.0 | 0.0 | 2.2 | 98%
 | a_slim | 0.06 | 0.0 | 1.0 | 0.1 | 1.0 | 8%
 | b_slim | 0.11 | 0.0 | 1.0 | 0.0 | 1.0 | 4%
 | a_switch | 0.64 | 0.0 | 1.0 | 0.1 | 0.9 | 20%
Table 1: Comparison of the original parameter ranges and the validated input region (IRD-derived hyperbox) identified using the PRIM method. The "IRD range" corresponds to the largest subregion where ≥90% of sampled configurations lead to valid, physically meaningful outputs from AlphaPEM.
Large range reductions for i0_c_ref, kappa_co, and kappa_c indicate these parameters must be tightly constrained to ensure valid polarization curves
Immutable features: fixed to reference value
Motivation
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
Resulting hyperbox from IRD

## Slide 13
# | Parameter | Description | Range
1 | Tfc | Desired fuel cell temperature (K) | [333, 363]
2 | Pa_des | Desired anode pressure (Pa) | [130000, 300000]
3 | Sc | Stoichiometric ratio of oxygen | [1.1, 3.0]
4 | Phi_c_des | Desired cathode relative humidity | [0.1, 0.7]
5 | epsilon_gdl | GDL porosity (dimensionless) | [0.55, 0.8]
6 | tau | Pore structure coefficient (dimensionless) | [1.0, 4.0]
7 | epsilon_mc | Volume fraction of ionomer in catalyst layer (dimensionless) | [0.15, 0.4]
8 | epsilon_c | Compression ratio of GDL (dimensionless) | [0.15, 0.3]
9 | e | Capillary exponent (integer) | {3, 4, 5}
10 | Re | Electron conduction resistance (Ω·m²) | [5.0e-7, 5.0e-6]
11 | i0_c_ref | Cathode exchange current density (A/m²) | [0.001, 80]
12 | kappa_co | Crossover correction coefficient (mol/(m·s·Pa)) | [15, 40]
13 | kappa_c | Overpotential correction exponent (dimensionless) | [0, 2.5]
Table 2: Final 13 input parameters for valid AlphaPEM simulations, selected in collaboration with project partners and AlphaPEM’s author Raphael Gass. Operating conditions were intentionally left unrestricted; undetermined physical parameters were fixed or constrained based on IRD-guided model validity analysis.
← Color palette for visualizations
The following parameters were fixed to simplify the model:
Sa = 1.3
Phi_a_des = 0.5
a_slim = 0
b_slim = 1
a_switch = 0.99
Pc_des is derived from Pa_des − 20000 Pa
Fixed parameters
Motivation
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
Final set of input parameters
for sampling of AlphaPEM

## Slide 14
3. Sensitivity Analysis (SA)
What features influence the
output the most?

## Slide 15
What is a sensitivity analysis?
It a collection of techniques used to evaluate feature effects It helps assess:
How changes in input variables influence the output of a model.
The robustness of the model to variations or uncertainty in those input features.
What is the goal?
Quantify the influence of each input on the output.
Prioritize the most impactful variables.
Guide model simplification
Increase understanding of the system's behavior under different conditions.
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis

## Slide 16
AlphaPEM is accurate, but simulations are computationally expensive.
Sensitivity analysis (especially Sobol) needs thousands of evaluations.
Not feasible to run AlphaPEM directly at that scale.
Surrogate model
Idea: We train fast, accurate models to approximate AlphaPEM
Compute SHAP values (model explainability).
Run Sobol analysis (variance decomposition).
Explore inputs cheaply and flexibly.
Region-based SA
Regions
definition
Activation [0;0.4)
Ohmic [0.4; 1.6)
Mass transport [1.6; Inf)
Advantages: Localized insights about most important features per region.
XGBoost
Random Forest
Figure 6: Current density regions in a polarization curve. Source: ResearchGate
Output for SA: We use the AUC of the polarization curve, computed within each region, as the target metric for Sobol analysis
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis

## Slide 17
1
AlphaPEM
Sobol Indices
High accuracy, efficient with large datasets, handles complex interactions well.
XGBoost
SHAP Values
Sobol Indices
2
Sobol Indices quantify how much of the output variance is due to each input (individually and via interactions).
SHAP values explain how much each feature contributes to a model’s prediction.
SA methods
It generates quasi-random sequences that are uniformly distributed sample points in high-dimensional spaces.
Sample strategy Sobol sequences
In the implementation we consider first order indices (S1) and second order interaction indices (S2)
Approaches
Random Forest
3
Robust to noise, less sensitive to hyperparameters, offers rough uncertainty estimates via tree variance.
Surrogates
Model based
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis

## Slide 18
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
1
AlphaPEM
Sobol Indices
Sobol Indices quantify how much of the output variance is due to each input (individually and via interactions).
SHAP values explain how much each feature contributes to a model’s prediction.
SA methods
It generates quasi-random sequences that are uniformly distributed sample points in high-dimensional spaces.
Sample strategy Sobol sequences
Approaches
High accuracy, efficient with large datasets, handles complex interactions well.
XGBoost
SHAP Values
Sobol Indices
2
Random Forest
3
Robust to noise, less sensitive to hyperparameters, offers rough uncertainty estimates via tree variance.
Surrogates
Model based
In the implementation we consider first order indices (S1) and second order interaction indices (S2)

## Slide 19
AlphaPEM: Sobol
S1-based Feature Ranking
Activation
Ohmic
Mass Transport
Figure 7: First-order Sobol (S1) sensitivity indices for the AlphaPEM model, grouped by current density region. Bars show the S1 value for each parameter, with black error bars indicating 95% confidence intervals. Rankings reflect the relative influence of each parameter.
For the Sobol’s implementation:
N = 1024 (sample size) → 28644 configurations
*Confidence is based on bootstrapping resampling
Metric | Activation | Ohmic | Mass Transport
S1 (only significant) | 0.970 | 0.932 | 0.879
S2 (only significant) | 0.000 | 0.000 | 0.000
Table 3: Sum of significant (CI does not contain 0) Sobol indices per region. Main effects account for nearly all the explained variance.
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis

## Slide 20
Figure 8: Rankings of the top 13 input parameters by total Sobol indices (ST) across current density regions. Rank 1 = most important. Lines show how parameter influence shifts between regions, highlighting stable drivers (e.g. i0_c_ref) and region-specific effects (e.g. Re).
Table 4. Rankings of features selected in each region based on first-order Sobol indices (S1). Features were included if their main effects cumulatively explained at least 85% of the variance in a region. Each entry shows the feature's ranking using S1 (1 = most important).
Feature | Activation | Ohmic | Mass transport
i0_c_ref | 1 | 1 | 1
kappa_c | 2 | 3 | 6
Tfc | 3 | 4 | 3
Pa_des |  | 2 | 2
Re |  |  | 4
tau |  |  | 5
epsilon_mc |  |  | 7
Accumulated S1 | 0.864 | 0.854 | 0.875
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
AlphaPEM: Sobol
Total Sobol (S1) Index–based Feature Importance

## Slide 21
Activation
AlphaPEM: Sobol
ST Index convergence (1)
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
Figure 9: Total Sobol indices (ST) for the Activation region as a function of Sobol base sample size N. Each curve shows how the ST estimate stabilizes as more configurations are used (up to N=1024, corresponding to 28,644 total evaluations).

## Slide 22
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
1
AlphaPEM
Sobol Indices
Sobol Indices quantify how much of the output variance is due to each input (individually and via interactions).
SHAP values explain how much each feature contributes to a model’s prediction.
SA methods
It generates quasi-random sequences that are uniformly distributed sample points in high-dimensional spaces.
Sample strategy Sobol sequences
In the implementation we consider first order indices (S1) and interaction indices (S2)
Approaches
High accuracy, efficient with large datasets, handles complex interactions well.
XGBoost
SHAP Values
Sobol Indices
2
Random Forest
3
Robust to noise, less sensitive to hyperparameters, offers rough uncertainty estimates via tree variance.
Surrogates
Model based

## Slide 23
XGBoost Performance
Data preparation
We are fitting the voltage as a function of the 13 features & the current density.
Only valid polarization curves (~54k configurations) and no negative voltages
Train the model
XGBoost with nested CV
Inner 3-fold CV: for tuning XGBoost hyperparameters.
Outer 5-fold CV: to assess generalization performance.
Metric | General | Activation | Ohmic | Mass transport
MAE* | 0.0150 ± 0.0002 | 0.0096 ± 0.0001 | 0.0129 ± 0.0002 | 0.0181 ± 0.0003 ​
RMSE* | 0.0013 ± 0.0000 | 0.0003 ± 0.0000 | 0.0010 ± 0.0000 | 0.0019 ± 0.0001
R-squared | 0.9549 ± 0.0015 | 0.9650 ± 0.0007 | 0.9229 ± 0.0033 | 0.8906 ± 0.0038
*Unit: Watts/cm²
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
Table 5: Generalization performance of the XGBoost model (nested CV, 5k valid samples).

## Slide 24
XGBoost Performance
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
Figure 10: Histogram of residuals from the XGBoost surrogate model for one outer fold. Zero-centered but shows some skew.
Figure 11: Boxplot of residuals from the XGBoost surrogate model across current density indices. Each box summarizes the prediction error distribution for a given point along the polarization curves.

## Slide 25
Data preparation
We are fitting the voltage as a function of the 13 features & the current density.
Only valid polarization curves (only 5k configurations) and no negative voltages
Train the model
RF with nested CV
Inner 3-fold CV: for tuning RF hyperparameters.
Outer 5-fold CV: to assess generalization performance.
Table 6: Generalization performance of the Random Forest model (nested CV, 5k valid samples).
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
RandomForest
Metric | General
MAE* | 0.0300 ± 0.0019
RMSE* | 0.0592 ± 0.0064
R-squared | 0.8846 ± 0.0220
*Unit: Watts/cm²

## Slide 26
Figure 12: Comparison of parameter rankings across current density regions based on SHAP values. Lines track changes in feature importance from activation to ohmic to mass transport regions, where a lower rank indicates higher influence on model output.
Union of all selected features across regions
The top 5 features in each region – 6 features
Pa_des
Re
Tfc
i0_c_ref
ifc
kappa_c
XGBoost SHAP
Rankings per
Region
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis

## Slide 27
Figure 13: Comparison of parameter rankings across current density regions based on Sobol values. Lines track changes in feature importance from activation to ohmic to mass transport regions, where a lower rank indicates higher influence on model output.
Union of all selected features across regions
Features selected based on S1 indices from Sobol analysis, explaining over 90% of total variance - 8 features
Pa_des
Re
Tfc
epsilon_mc
i0_c_ref
ifc
kappa_c
Tau
XGBoost Sobol
Rankings per
Region
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis

## Slide 28
Feature | Activation | Ohmic | Mass transport
i0_c_ref | 1 | 1 | 1
ifc | 2 | 2 | 2
kappa_c | 3 | 5 | 7
Tfc | 4 | 4 | 4
Pa_des | 5 | 3 | 3
Re |  |  | 5
tau |  | 6 | 6
Epsilon_mc |  |  | 8
Accumulated S1 | 0,928 | 0,908 | 0,904
Sobol (S1)
Feature | Activation | Ohmic | Mass transport
ifc | 1 | 1 | 1
i0_c_ref | 2 | 2 | 2
kappa_c | 3 | 5 | 
Tfc | 4 | 4 | 4
Pa_des | 5 | 3 | 3
Re |  |  | 5
Mean |SHAP|
Table 8: Ranking position of selected features based on total Sobol index across polarization regions. Features are selected so that the accumulated S1 equals a threshold (0.9).
Table 7: Ranking positions of selected features based on SHAP values across polarization regions. The top 5 features in each region are displayed.
Common features (intersection):
Pa_des, Re, Tfc, i0_c_ref, ifc , kappa_c
Adittional features: epsilon_mc, tau (Sobol)
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
XGBoost Comparing
Rankings per
Region

## Slide 29
4. Surrogate Model
Building a more efficient, faithful and closed-form surrogate

## Slide 30
PySR: Symbolic Regression in Python
Goal: find a mathematical expression that best fits the data
Discovers both the form and the parameters of the model
Expressions are represented as trees
Assumptions on the functional form can be included.
Uses evolutionary algorithms
Source: Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl
Figure 14: Example of how an expression is represented as a tree. Source: Wikimedia
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Cranmer (2023)

## Slide 31
Mutation
Crossover
Figure 15: Example of symbolic expression mutation in PySR.
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Simplification
Y
+
Y
3
+
5
8
Figure 16: Example of symbolic expression simplification in PySR. PySR applies such simplifications to produce more compact and interpretable symbolic models.
Figure 17: Example of symbolic expression crossover in PySR
Source: Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl
PySR Operations
2Y

## Slide 32
Population of expressions is randomly sampled
Select best expressions
Winner is selected for breeding
    Mutation
    Crossover
    Simplification
    Constant optimization
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
PySR Inner Loop
Figure 18: Vizualization of the PySR inner loop.
Source: Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl

## Slide 33
Multiple populations evolve independently
At the end of a specified number of evolution iterations migration between islands is performed.
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
PySR Outer Loop
Figure 19: Vizualization of the PySR outer loop.
Source: Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl

## Slide 34
Experimental Setup for Symbolic Regression
Data: Filtered only polarization curves that have only positive voltage (≈ 53 000 curves)
80-20 train test split with grouping (each curve in either train or test set)
Binary operators: +, -, *, /
Unary operators: exp, log, square, cube, inv, neg
Loss: L2 Distance Loss
Training with batches
Unconstrained search space
No restriction in the form of the learned equation
Constrained search space (Physics-informed)
Equations are constrained to look like:
Where a, b, c, d, e are equations to be learned by PySR
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Approaches for symbolic regression

## Slide 35
SHAP for the best-performing equations
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Figure 20: Mean absolute SHAP values for each feature, indicating their average contribution to the model's output.
Unconstrained
Physics-informed
R² = 0.854
MSE = 0.0042
R² = 0.884
MSE = 0.0032

## Slide 36
5. Future Work

## Slide 37
Surrogate Model
Try out additional physics informed methods:
    Deep Symbolic Regression.
    End-to-end symbolic regression with transformers.
Increase the training time for the Symbolic Regression.
Include physical constraints in PySR.
Perform hyperparameter tunning in PySR.
(Petersen et al.)
(Kamienny et al.)
  Run the Sensitivity Analysis with Sobol with a larger dataset to improve the confidence intervals of the Sobol indices.
  Dynamic definition of the regions, based on the shape rather than in a fixed current.
Motivation | Model Validity | Sensitivity Analysis | Surrogate Model
5. Future Work
Future work
Sensitivity Analysis

## Slide 38
Bibliography

## Slide 39
Dandl, S., Casalicchio, G., Bischl, B., & Bothmann, L. (2023). Interpretable Regional Descriptors: Hyperbox-Based Local Explanations (arXiv:2305.02780) [Preprint]. arXiv. https://doi.org/10.48550/arXiv.2305.02780
Gass, R., Li, Z., Outbib, R., Jemei, S., & Hissel, D. (2024). AlphaPEM: An open-source dynamic 1D physics-based PEM fuel cell model for embedded applications [Preprint]. SoftwareX. https://doi.org/10.48550/arXiv.2407.12373
Safjan, K. (2023). KernelShap and TreeShap – Two Most Popular Variations of the SHAP Method. Safjan Blog. Retrieved from https://safjan.com/kernelshap-treeshap-two-most-popular-variations-of-the-shap-method/
Gass, R. (2024). Advanced physical modeling of PEM fuel cells to enhance their performances [Doctoral dissertation, Aix Marseille University (AMU)]. Computational Physics [physics.comp-ph]. https://theses.hal.science/tel-04923016
Cranmer, M (2023). Interpretable Machine Learning for Science with PySR and SymbolicRegression.jl,, arXiv: arXiv:2305.01582. Accessible: http://arxiv.org/abs/2305.01582
Petersen, B. K. (2021)Deep symbolic regression: Recovering mathematical expressions from data via risk-seeking policy gradients. https://arxiv.org/abs/1912.04871
Kammieny, PA (2022) End-to-end symbolic regression with transformers https://arxiv.org/pdf/2204.10532
Bibliography

## Slide 40
Thanks!
We’re happy to answer your questions

## Slide 41
Appendix

## Slide 42
Index of the appendix
  Slide 47: How PRIM finds a valid input region in AlphaPEM
  Slide 48: Sobol Indices
  Slide 49: SHAP values
  Slide 50: TreeSHAP
  Slide 51: Pros vs. Cons Sobol vs SHAP values
  Slide 53: Sobol sequences
  Slide 54: AlphaPEM detail Sobol S1
  Slide 55: AlphaPEM Sobol ranking ST
  Slide 56: AlphaPEM detail Sobol ST
  Slide 57: AlphaPEM Sobol convergence ST - Ohmic
  Slide 58: AlphaPEM Sobol convergence ST - Mass Transport
  Slide 59: AlphaPEM Sobol ranking comparison ST
  Slide 60: XGBoost hyperparameter tuning
  Slide 61: XGBoost SHAP – Activation
  Slide 62: XGBoost Sobol S1– Activation
  Slide 63: XGBoost Sobol convergence ST– Activation
  Slide 64: XGBoost SHAP – Ohmic
  Slide 65: XGBoost Sobol S1– Ohmic
  Slide 66: XGBoost Sobol convergence ST– Ohmic
  Slide 67: XGBoost SHAP – Mass Transport
  Slide 68: XGBoost Sobol S1 – Mass Transport
  Slide 69: XGBoost Sobol convergence ST– Mass Transport

## Slide 43
Motivation
Sensitivity Analysis | Surrogate Model | Future Work
2. Model Validity
How PRIM finds a valid input region in AlphaPEM
Start with all data (both valid and invalid points)
Peeling phase:
  Gradually shrink the box by removing slices (e.g., lowest 5% of temperature or highest 5% of pressure)
  Keep only slices that increase prediction precision (proportion of valid configs)
Stop when precision = 1: when all predictions inside are valid)
Pasting phase:
  Try adding slices back (if they don’t reduce precision)
PRIM Steps
Figure: Valid input region (blue) found by PRIM around the reference point (★); only includes configurations with valid polarization curves.

## Slide 44
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD
Sobol Indices
Sobol analysis assumes the model can be decomposed additively
First-order (S1) : Individual effect
Since the model is decomposed this way, the total variance of the output can be split into components.
Sobol indices quantify how much of the output variance is due to each input (individually and via interactions).
Total-order (ST): Total effect including interactions
Second-order (S2):
pairwise interactions
Back to SA
Source: Advanced Machine Learning course material

## Slide 45
SHAP Values
is a game theory-based framework that assigns each feature a value reflecting its contribution to a model’s prediction.
SHAP considers all possible subsets of features and computes the marginal contribution of a feature when added to each subset.
This ensures three key properties:
Local accuracy: the sum of SHAP values equals the model output.
Consistency: increasing a feature's impact in the model cannot decrease its SHAP value.
Missingness: features not used in a prediction receive zero contribution.
SHAP values show how much a single feature changes the model’s average prediction when we know the value of that feature.
1
2
3
SHAP value for a feature tells you: "How much does this feature shift the prediction away from the average when it's known?
SHAP (SHapley Additive exPlanations)
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 46
TreeSHAP
(for Trees and Forests)
TreeSHAP efficiently computes exact Shapley values for tree-based models by exploiting the tree structure to avoid enumerating all feature subsets.
Algorithm
Advantages:
It computes the exact Shapley values without the need for sampling or approximations
It is computationally efficient due to its dynamic programming approach.
It is specifically designed for tree-based models, which are widely used in practice.
Back to SA
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 47
Pros & cons
Sobol Indices
SHAP Values
Global sensitivity quantifies how inputs influence output variance.
Accounts for interactions.
Applies to any model.
Offers a clear variance decomposition.
Local explanations clarify individual predictions.
Applies to any model.
Handle interactions.
They are grounded in fair game-theoretic principles, with guarantees of fairness and consistency.
High computational cost.
Assumes input independence.
Provides only global insights.
Struggles with high-dimensional data.
Computationally intensive.
May give misleading results if feature dependence isn't handled well.
Back to SA
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 48
Sampling strategy: Sobol sequences
It generates quasi-random sequences that are uniformly distributed sample points in high-dimensional spaces.
Calculating the Sobol indices over those configurations lead into more stable and consistent results, due to the uniformity of the samples.
They allow incrementally increase the sample size, while preserving and building upon previous points saving computing time.
Back to SA
Sobol’s implementation
Sample size
  For calculating only first-order indices (S1): N × (D + 2)
  For both first-order (S1) and second-order (S2) indices: N × (2D + 2)
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 49
AlphaPEM: Sobol
For the Sobol’s implementation:
N = 1024 (sample size) → 28644 configurations
*Confidence is based on bootstrapping-like resampling
S1 Indices
Table XX: First-order Sobol indices (S1) with 95% bootstrapped confidence intervals for each input parameter across the three current density regions of the AlphaPEM model. Rankings indicate relative importance within each region.
 | Activation |  | Ohmic |  | Mass Transport | 
Parameter | S1 index CI (95%) | Ranking | S1 index CI (95%) | Ranking | S1 index CI (95%) | Ranking
i0_c_ref | 0.550 ± 0.09 | 1 | 0.429 ± 0.08 | 1 | 0.325 ± 0.07 | 1
kappa_c | 0.229 ± 0.05 | 2 | 0.136 ± 0.03 | 3 | 0.043 ± 0.02 | 6
Tfc | 0.085 ± 0.03 | 3 | 0.133 ± 0.04 | 4 | 0.144 ± 0.03 | 3
Pa_des | 0.059 ± 0.03 | 4 | 0.156 ± 0.04 | 2 | 0.176 ± 0.04 | 2
kappa_co | 0.024 ± 0.01 | 5 | 0.003 ± 0.01 | 10 | 0.000 ± 0.00 | 9
tau | 0.005 ± 0.01 | 7 | 0.030 ± 0.02 | 5 | 0.062 ± 0.02 | 5
Re | 0.002 ± 0.00 | 9 | 0.023 ± 0.01 | 6 | 0.087 ± 0.03 | 4
epsilon_mc | 0.002 ± 0.01 | 10 | 0.015 ± 0.01 | 7 | 0.037 ± 0.02 | 7
Phi_c_des | 0.000 ± 0.00 | 13 | 0.004 ± 0.01 | 8 | 0.005 ± 0.01 | 8
epsilon_gdl | 0.001 ± 0.00 | 11 | -0.001 ± 0.00 | 12 | -0.005 ± 0.01 | 12
epsilon_c | 0.001 ± 0.00 | 12 | -0.001 ± 0.00 | 13 | -0.005 ± 0.00 | 13
Sc | 0.008 ± 0.01 | 6 | 0.000 ± 0.01 | 11 | -0.002 ± 0.01 | 11
e | 0.004 ± 0.01 | 8 | 0.003 ± 0.02 | 9 | -0.000 ± 0.02 | 10
Sum | 0.97 |  | 0.93 |  | 0.867 | 
Avg Conf | 0.0192 |  | 0.0216 |  | 0.0228 | 
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 50
Surrogate Model | Future Work
3. Sensitivity Analysis
Motivation | Model validity
AlphaPEM: Sobol
ST-based Feature Ranking
Activation
Ohmic
Mass Transport
Figure XX: Total Sobol (ST) sensitivity indices for the AlphaPEM model, grouped by current density region: Activation, Ohmic, and Mass Transport. Bars show the ST value for each parameter, with black error bars indicating 95% confidence intervals. Rankings reflect the relative influence of each parameter within the region.
For the Sobol’s implementation:
N = 1024 (sample size) → 28644 configurations
*Confidence is based on bootstrapping-like resampling

## Slide 51
AlphaPEM: Sobol
For the Sobol’s implementation:
N = 1024 (sample size) → 28644 configurations
*Confidence is based on bootstrapping-like resampling
ST Indices
Table XX: Total Sobol indices (ST) with 95% bootstrapped confidence intervals for each input parameter across the three current density regions of the AlphaPEM model. Rankings indicate relative importance within each region.
 | Activation |  | Ohmic |  | Mass Transport | 
Parameter | ST index | Ranking | ST index | Ranking | ST index | Ranking
i0_c_ref | 0.550 ± 0.09 | 1 | 0.429 ± 0.08 | 1 | 0.325 ± 0.07 | 1
kappa_c | 0.229 ± 0.05 | 2 | 0.136 ± 0.03 | 3 | 0.043 ± 0.02 | 6
Tfc | 0.085 ± 0.03 | 3 | 0.133 ± 0.04 | 4 | 0.144 ± 0.03 | 3
Pa_des | 0.059 ± 0.03 | 4 | 0.156 ± 0.04 | 2 | 0.176 ± 0.04 | 2
kappa_co | 0.024 ± 0.01 | 5 | 0.003 ± 0.01 | 10 | 0.000 ± 0.00 | 9
tau | 0.005 ± 0.01 | 7 | 0.030 ± 0.02 | 5 | 0.062 ± 0.02 | 5
Re | 0.002 ± 0.00 | 9 | 0.023 ± 0.01 | 6 | 0.087 ± 0.03 | 4
epsilon_mc | 0.002 ± 0.01 | 10 | 0.015 ± 0.01 | 7 | 0.037 ± 0.02 | 7
Phi_c_des | 0.000 ± 0.00 | 13 | 0.004 ± 0.01 | 8 | 0.005 ± 0.01 | 8
epsilon_gdl | 0.001 ± 0.00 | 11 | -0.001 ± 0.00 | 12 | -0.005 ± 0.01 | 12
epsilon_c | 0.001 ± 0.00 | 12 | -0.001 ± 0.00 | 13 | -0.005 ± 0.00 | 13
Sc | 0.008 ± 0.01 | 6 | 0.000 ± 0.01 | 11 | -0.002 ± 0.01 | 11
e | 0.004 ± 0.01 | 8 | 0.003 ± 0.02 | 9 | -0.000 ± 0.02 | 10
Sum | 0.97 |  | 0.93 |  | 0.867 | 
Avg Conf | 0.0192 |  | 0.0216 |  | 0.0228 | 
Surrogate Model | Future Work
3. Sensitivity Analysis
Motivation | Model validity

## Slide 52
AlphaPEM: Sobol
ST Index convergence (2)
Ohmic
Figure: Total Sobol indices (ST) for the Ohmic region as a function of Sobol base sample size N. Each curve shows how the ST estimate stabilizes as more configurations are used (up to N=1024, corresponding to 28,644 total evaluations). This helps assess the reliability and convergence behavior of the sensitivity estimates per parameter.
Surrogate Model | Future Work
3. Sensitivity Analysis
Motivation | Model validity

## Slide 53
AlphaPEM: Sobol
ST Index convergence (3)
Mass transport
Figure: Total Sobol indices (ST) for the Mass transport region as a function of Sobol base sample size N. Each curve shows how the ST estimate stabilizes as more configurations are used (up to N=1024, corresponding to 28,644 total evaluations). This helps assess the reliability and convergence behavior of the sensitivity estimates per parameter.
Surrogate Model | Future Work
3. Sensitivity Analysis
Motivation | Model validity

## Slide 54
AlphaPEM: Sobol
Total Sobol (ST) Index–based Feature Importance
Figure: Ranking of the top 13 input parameters based on total Sobol indices (ST) across the three current density regions of the AlphaPEM model. Rank 1 indicates the most influential parameter in a given region. Lines track how each parameter’s importance changes between regions, revealing stable drivers (e.g., i_0c_ref​​) and region-specific effects (e.g. Re).
Surrogate Model | Future Work
3. Sensitivity Analysis
Motivation | Model validity

## Slide 55
Data preparation
We are fitting the voltage as a function of the 13 features & the current density.
Only valid polarization curves (~55k configurations)
Train the model
XGBoost with nested CV
Inner 3-fold CV: for tuning XGBoost hyperparameters.
Outer 5-fold CV: to assess generalization performance.
XGBRegressor
n_estimators: [300, 500, 700]
max_depth: [6, 8, 10]
learning_rate: [0.01, 0.05]
subsample: [0.8, 1.0]
colsample_bytree: [0.8, 1.0]
Best configuration
colsample_bytree: 0.8
learning_rate: 0.05
max_depth: 8
n_estimators: 700
subsample: 0.8
Back to XGBoost
Motivation | Model Validity
Surrogate Model | Future Work
3. Sensitivity Analysis
XGBoost hyperparameter tuning

## Slide 56
SHAP
Feature
Importance
XGBoost
Activation
Summary plot
Feature importance
Figure XX: SHAP feature importance ranking based on the XGBoost model, showing the top contributors to the output in the Activation region.
Figure XX: SHAP summary plot showing feature impact on the XGBoost model for the Activation region. Color indicates feature value; horizontal spread reflects influence.
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 57
Sobol
XGBoost
Activation
N = 8.192
→ 245,760 configurations
Sum S1 = 0.9547
Sum S2 = 0.0830
Sum S1 + S2 = 1.0377
Sum ST = 1.0665
Feature | S1 | S1 CI | ST | ST CI | S2 Total | S2 CI
i0_c_ref | 0.4344 | (0.41, 0.459) | 0.4422 | (0.425, 0.459) | 0.0050 | (-0.119, 0.129)
kappa_c | 0.1834 | (0.169, 0.198) | 0.2108 | (0.202, 0.219) | -0.0006 | (-0.021, 0.019)
ifc | 0.1870 | (0.175, 0.199) | 0.1939 | (0.186, 0.202) | 0.0000 | (0.0, 0.0)
Tfc | 0.0768 | (0.068, 0.086) | 0.0818 | (0.079, 0.085) | 0.0018 | (-0.184, 0.187)
Pa_des | 0.0466 | (0.038, 0.055) | 0.0739 | (0.07, 0.078) | 0.0725 | (-0.078, 0.223)
kappa_co | 0.0098 | (0.006, 0.014) | 0.0183 | (0.017, 0.019) | 0.0114 | (-0.001, 0.024)
Sc | 0.0057 | (0.003, 0.009) | 0.0136 | (0.013, 0.014) | 0.0070 | (-0.044, 0.058)
tau | 0.0040 | (0.001, 0.007) | 0.0095 | (0.009, 0.01) | -0.0069 | (-0.041, 0.028)
epsilon_mc | 0.0032 | (0.001, 0.006) | 0.0071 | (0.007, 0.007) | -0.0007 | (-0.027, 0.026)
Re | 0.0017 | (-0.001, 0.004) | 0.0056 | (0.005, 0.006) | 0.0007 | (-0.013, 0.014)
Phi_c_des | 0.0024 | (0.001, 0.004) | 0.0046 | (0.004, 0.005) | -0.0168 | (-0.048, 0.014)
epsilon_gdl | -0.0003 | (-0.002, 0.001) | 0.0026 | (0.002, 0.003) | 0.0070 | (-0.014, 0.028)
epsilon_c | -0.0005 | (-0.002, 0.001) | 0.0023 | (0.002, 0.002) | 0.0052 | (-0.007, 0.017)
e | 0.0004 | (-0.0, 0.001) | 0.0004 | (0.0, 0.0) | -0.0027 | (-0.007, 0.002)
Figure XX: Sobol sensitivity indices for the Activation region based on the XGBoost model, showing first-order (S1), total-order (ST), and second-order (S2) effects with confidence intervals. Parameters i0_ref, κ_c, and ifc exhibit the highest influence on model output.
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 58
Sobol
ST
XGBoost
Activation
N = 8.192
→ 245,760 configurations
Sum S1 = 0.9547
Sum S2 = 0.0830
Sum S1 + S2 = 1.0377
Sum ST = 1.0665
Figure XX: Convergence of total-order (ST) Sobol indices for features in the Activation region across increasing sample sizes. The indices stabilize as sample size grows, with i0'_c ref, κ_c, and ifc showing the highest total contributions to output variance.
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 59
SHAP
Feature
Importance
XGBoost
Summary plot
Feature importance
Ohmic
Figure XX: SHAP feature importance ranking based on the XGBoost model, showing the top contributors to the output in the Ohmic region.
Figure XX: SHAP summary plot showing feature impact on the XGBoost model for the Ohmic region. Color indicates feature value; horizontal spread reflects influence.
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 60
Sobol
XGBoost
N = 8.192
→ 245,760 configurations
Sum S1 = 0.9464
Sum S2 = 0.0675
Sum S1 + S2 = 1.0139
Sum ST = 1.0799
Feature | S1 | S1 CI | ST | ST CI | S2 Total | S2 CI
i0_c_ref | 0.3046 | (0.285, 0.324) | 0.3145 | (0.3, 0.329) | 0.0055 | (-0.089, 0.1)
ifc | 0.2770 | (0.262, 0.292) | 0.2881 | (0.277, 0.299) | 0.0000 | (0.0, 0.0)
Pa_des | 0.1069 | (0.096, 0.118) | 0.1319 | (0.126, 0.138) | 0.0479 | (-0.158, 0.254)
kappa_c | 0.0958 | (0.085, 0.107) | 0.1191 | (0.114, 0.124) | 0.0007 | (-0.016, 0.017)
Tfc | 0.1050 | (0.095, 0.115) | 0.1164 | (0.112, 0.121) | 0.0102 | (-0.193, 0.213)
tau | 0.0183 | (0.014, 0.023) | 0.0286 | (0.027, 0.03) | 0.0088 | (-0.049, 0.066)
Re | 0.0151 | (0.01, 0.02) | 0.0231 | (0.022, 0.024) | 0.0026 | (-0.025, 0.031)
epsilon_mc | 0.0116 | (0.007, 0.016) | 0.0193 | (0.018, 0.02) | -0.0039 | (-0.047, 0.039)
Phi_c_des | 0.0083 | (0.005, 0.012) | 0.0151 | (0.014, 0.016) | -0.0051 | (-0.058, 0.048)
Sc | 0.0017 | (-0.001, 0.004) | 0.0096 | (0.009, 0.01) | -0.0058 | (-0.047, 0.036)
kappa_co | 0.0020 | (-0.0, 0.004) | 0.0063 | (0.006, 0.007) | 0.0023 | (-0.004, 0.009)
epsilon_gdl | 0.0003 | (-0.002, 0.002) | 0.0039 | (0.003, 0.004) | 0.0051 | (-0.021, 0.031)
epsilon_c | -0.0004 | (-0.002, 0.001) | 0.0034 | (0.003, 0.004) | 0.0008 | (-0.014, 0.016)
e | 0.0003 | (-0.0, 0.001) | 0.0005 | (0.0, 0.001) | -0.0016 | (-0.006, 0.003)
Figure XX: Sobol sensitivity indices for the Ohmic region based on the XGBoost model, showing first-order (S1), total-order (ST), and second-order (S2) effects with confidence intervals. Parameters i0_ref, κ_c, and ifc exhibit the highest influence on model output.
Ohmic
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 61
Sobol
ST
XGBoost
Figure XX: Convergence of total-order (ST) Sobol indices for features in the Ohmic region across increasing sample sizes. The indices stabilize as sample size grows, with i0'_c ref, κ_c, and ifc showing the highest total contributions to output variance.
N = 8.192
→ 245,760 configurations
Sum S1 = 0.9464
Sum S2 = 0.0675
Sum S1 + S2 = 1.0139
Sum ST = 1.0799
Ohmic
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 62
SHAP
Feature
Importance
XGBoost
Summary plot
Feature importance
Figure XX: SHAP feature importance ranking based on the XGBoost model, showing the top contributors to the output in the Mass Transport region.
Figure XX: SHAP summary plot showing feature impact on the XGBoost model for the Mass Transport region. Color indicates feature value; horizontal spread reflects influence.
Mass Transport
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 63
Sobol
XGBoost
N = 8.192
→ 245,760 configurations
Sum S1 = 0.9217
Sum S2 = 0.0510
Sum S1 + S2 = 0.9727
Sum ST = 1.1068
Feature | S1 | S1 CI | ST | ST CI | S2 Total | S2 CI
i0_c_ref | 0.2734 | (0.255, 0.291) | 0.2852 | (0.272, 0.299) | 0.0044 | (-0.08, 0.089)
ifc | 0.1726 | (0.161, 0.185) | 0.1863 | (0.179, 0.194) | 0.0000 | (0.0, 0.0)
Pa_des | 0.1524 | (0.14, 0.165) | 0.1853 | (0.178, 0.193) | 0.0381 | (-0.203, 0.28)
Tfc | 0.1282 | (0.118, 0.139) | 0.1486 | (0.142, 0.155) | -0.0148 | (-0.232, 0.203)
Re | 0.0696 | (0.06, 0.079) | 0.0830 | (0.08, 0.086) | 0.0045 | (-0.05, 0.059)
kappa_c | 0.0361 | (0.028, 0.044) | 0.0608 | (0.058, 0.063) | 0.0023 | (-0.009, 0.013)
tau | 0.0426 | (0.036, 0.049) | 0.0550 | (0.052, 0.058) | 0.0069 | (-0.066, 0.08)
epsilon_mc | 0.0290 | (0.022, 0.036) | 0.0395 | (0.038, 0.041) | -0.0114 | (-0.076, 0.053)
Phi_c_des | 0.0104 | (0.006, 0.015) | 0.0235 | (0.021, 0.025) | -0.0081 | (-0.076, 0.06)
Sc | 0.0047 | (0.001, 0.009) | 0.0190 | (0.018, 0.02) | 0.0176 | (-0.046, 0.082)
epsilon_gdl | 0.0010 | (-0.002, 0.004) | 0.0093 | (0.009, 0.01) | 0.0076 | (-0.032, 0.047)
kappa_co | 0.0023 | (-0.0, 0.005) | 0.0057 | (0.005, 0.006) | -0.0004 | (-0.007, 0.006)
epsilon_c | -0.0009 | (-0.003, 0.001) | 0.0048 | (0.004, 0.006) | 0.0066 | (-0.011, 0.025)
e | 0.0003 | (-0.001, 0.001) | 0.0008 | (0.001, 0.001) | -0.0022 | (-0.009, 0.005)
Figure XX: Sobol sensitivity indices for the Mass Transport region based on the XGBoost model, showing first-order (S1), total-order (ST), and second-order (S2) effects with confidence intervals. Parameters i0_ref, Pa_des, and ifc exhibit the highest influence on model output.
Mass Transport
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 64
Sobol
ST
XGBoost
Figure XX: Convergence of total-order (ST) Sobol indices for features in the Mass transport region across increasing sample sizes. The indices stabilize as sample size grows, with i0'_c ref, Pa_des, and ifc showing the highest total contributions to output variance.
N = 8.192
→ 245,760 configurations
Sum S1 = 0.9217
Sum S2 = 0.0510
Sum S1 + S2 = 0.9727
Sum ST = 1.1068
Mass Transport
Surrogate Model | Conclusions and next steps
3. Sensitivity Analysis
Introduction and motivation | IRD

## Slide 65
Equation | R² | MSE
 | 0.854 | 0.0042
 | 0.8496 | 0.0043
 | 0.8473 | 0.0043
 | 0.8329 | 0.0048
 | 0.828 | 0.0049
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Top 5 Equations for PySR with unconstrained search space
Table 9: Top 5 equations based on R² with unconstrained search space.

## Slide 66
Figure 21: Residuals of the best equation for different current density values. Residuals increase with the current density.
Figure 22: Histogram of the residuals of the best equation.
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Residuals for the equation with the best R² (unconstrained)

## Slide 67
Equation | R² | MSE
 | 0.884 | 0.0032
 | 0.884 | 0.0032
 | 0.884 | 0.0032
 | 0.8749 | 0.0036
 | 0.8735 | 0.0038
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model
Top 5 Equations for PySR with constrained search space (physics- informed)
Table 10: Top 5 equations based on R² with constrained search space (physics-informed).

## Slide 68
Residuals for the equation with the best R² (physics-informed)
Figure 23: Residuals of the best equation for different current density values. Residuals increase with the current density.
Figure 24: Histogram of the residuals of the best equation.
Motivation | Model Validity | Sensitivity Analysis
Future Work
4. Surrogate Model